## Slide 1: CLI AUTOMATION

## Slide 2
Ip sla 1
Icmp-echo x.x.x.x source-ip x.x.x.x
Frequency x
Ip sla schedule 1 start now life forever
22.255.200.13
22.255.200.14

## Slide 3
Ip sla 1
Icmp-echo x.x.x.x source-interface xxx
Frequency x
Ip sla schedule 1 start now life forever
22.255.200.14
G0/0/1.96

## Slide 4
Show ip sla statistics
22.255.200.13
22.255.200.14

## Slide 5
Show ip sla configuration
22.255.200.13
22.255.200.14

## Slide 6
Track 10 ip sla 1
Show track
INT LO 100
192.168.100.1
G0/1 – 10.0.0.1

## Slide 7
Ip sla 1
Icmp-echo 192.168.100.1 source-ip 10.0.0.1
Frequency 5
Ip sla 2
Icmp-echo 192.168.200.1 source-interface g0/1
Frequncy 10
Ip sla schedule 1 start now lifetime forever
Ip sla schedule 2 start now lifetime forever
INT LO 100
192.168.100.1
G0/1 – 10.0.0.1
INT LO 200
192.168.200.1

## Slide 8
Track 10 ip sla 1
Track 50 ip sla 2
Track 77 list Boolean or
Object 10
Object 50
Track 78 list Boolean and
Object 10 not
Object 50
Track 79 list Boolean or
Object 10 not
Object 50 not
INT LO 100
192.168.100.1
G0/1 – 10.0.0.1
INT LO 200
192.168.200.1

## Slide 9
Track 10 ip sla 1
Track 50 ip sla 2
Track 77 list Boolean or
Object 10
Object 50
Track 78 list Boolean and
Object 10 not
Object 50
Track 79 list Boolean or
Object 10 not
Object 50 not
INT LO 100
192.168.100.1
G0/1 – 10.0.0.1
INT LO 200
192.168.200.1
Event manager applet WOBC-RC
Event track 10 state down
Action 1.0 cli command “enable”
Action 2.0 cli command “config t”
Action 3.0 cli command “interface g0/0”
Action 4.0 cli command “shutdown”
Action 5.0 syslog msg ARTILLERY_LAN_DOWN
Event manager applet WOBC-RC_1
Event track 10 state up
Action 1.0 cli command “enable”
Action 2.0 cli command “config t”
Action 3.0 cli command “interface g0/0”
Action 4.0 cli command “no shutdown”
Action 5.0 syslog msg ARTILLERY_LAN_OPERATIONAL
G0/0 – 1.1.1.1
ARTILLERY LAN

## Slide 10
WHAT IS HAPPENING IN THE BACKGROUND?
STEP 1. THE IP SLAs THAT ARE BEING MONITORED BY TRACK 77 STOP RETURNING A CODE OF “OK”
STEP 2. THE STATE OF TRACK 77 GOES FROM UP TO DOWN
STEP 3. THE EVENT MANAGER EXECUTES THE SERIES OF “ACTION” COMMANDS IN NUMERICAL ORDER

## Slide 11
Track 10 ip sla 1
Track 50 ip sla 2
Track 77 list Boolean or
Object 10
Object 50
Track 78 list Boolean and
Object 10 not
Object 50
Track 79 list Boolean or
Object 10 not
Object 50 not
INT LO 100
192.168.100.1
G0/1 – 10.0.0.1
INT LO 200
192.168.200.1
Event manager applet EIGRP-BUILDER
Event track 78 state up
Action 1.0 cli command “enable”
Action 2.0 cli command “config t”
Action 3.0 cli command “router eigrp TESTING”
Action 4.0 cli command “address-fam ipv4 uni auton 1”
Action 5.0 cli command “network 10.0.0.0 0.0.0.3”
Action 6.0 cli command “network 1.1.1.0 0.0.0.255”
Action 7.0 cli command “topology base”
Action 8.0 cli command “distribute-list 10 in g0/1”
Action 9.0 syslog msg EIGRP-IS-IN-EFFECT
Event manager applet EIGRP-REMOVAL
Event track 78 state down
Action 1.0 cli command “enable”
Action 2.0 cli command “config t”
Action 3.0 cli command “no router eigrp TESTING”
G0/0 – 1.1.1.1
ARTILLERY LAN

## Slide 12
Track 10 ip sla 1
Track 50 ip sla 2
Track 77 list Boolean or
Object 10
Object 50
Track 78 list Boolean and
Object 10 not
Object 50
Track 79 list Boolean or
Object 10 not
Object 50 not
INT LO 100
192.168.100.1
G0/1 – 10.0.0.1
INT LO 200
192.168.200.1
Event manager applet EIGRP-BUILDER
Event track 78 state up
Action 1.0 cli command “enable”
Action 2.0 cli command “config t”
Action 3.0 cli command “router eigrp TESTING”
Action 4.0 cli command “address-fam ipv4 uni auton 1”
Action 5.0 cli command “network 10.0.0.0 0.0.0.3”
Action 6.0 cli command “network 1.1.1.0 0.0.0.255”
Action 7.0 cli command “topology base”
Action 8.0 cli command “distribute-list 10 in g0/1”
Action 9.0 syslog msg EIGRP-IS-IN-EFFECT
Event manager applet EIGRP-BUILDER
Action 6.5 cli command “network 2.2.2.0 0.0.0.255”
G0/0 – 1.1.1.1
ARTILLERY LAN
G0/2 – 2.2.2.1/24

## Slide 13
R1#
Config t
Alias exec x1 show ip int brief
Alias exec x2 show ip route
Alias exec x3 show ip ospf neighbor
Alias exec b1 show bgp vpnv6 vrf BGP-NEIGHBORS unicast summary | incl 22.228.0.1
Alias configure e9 router eigrp 9
Alias configure t9 interface tunnel 97009
Alias configure a1 ip access-list extended INBOUND-TRAFFIC
Alias exec RESET tclsh reset.base-config.tbc

## Slide 14
R1#
Config t
Alias exec x3 show ip ospf neighbor

## Slide 15
R1#
Config t
Alias configure a1 ip access-list extended INBOUND-TRAFFIC