## Slide 1: MPLS OVERVIEW

## Slide 2
Why MPLS?
Logical separation of traffic can be imposed at the PE, and maintained through the Service Provider Core
  VRF’s, Multi-protocol BGP
The use of one unified network infrastructure
  Hybrid systems of IP / ATM / Frame-Relay are unnecessary
  MPLS encapsulation can contain a variety of payloads, IP, IPv6, Ethernet, HDLC, PPP
    L3VPN, VPLS, Pseudowire, etc.
Optimal / Flexible traffic flow
  SP Core network IGP will dynamically determine best path vs. static assignments (Frame-Relay / ATM)
  SP networks can implement static LSP determination (Traffic Engineering)
Notes: one unified network
- MPLS is multiprotocol, so it can carry a variety of payloads, IP, IPv6, Ethernet, HDLC, PPP
BGP free core
- BGP requires a lot of memory and CPU cycles, it is much easier to not use BGP in the core, only on the edge devices
Peer-to-peer model
- provider edge routers will peer with the customer edge router, making overall configuration and troubleshooting easier
Optimal traffic flow
- the provider’s IGP will chose the best path across the core, without having to configure virtual circuits for every connection

## Slide 3
Dynamic traffic flow
  the provider’s IGP will chose the best path across the core, without having to configure virtual circuits for every connection
Traffic Engineering – RSVP-TE
  The ability to assign traffic to links that not the “best path” to make usage of all the links in the core
  Gives us the ability to map one FEC (LSP) traffic over SATCOM and another FEC over LOS
  Adds the ability to do source routing
  MPLS-TE Fast Reroute (FRR)
  Attribute flag tunneling
Benefits of MPLS

## Slide 4
G0/0/1
G0/0/1
R-1
R-2
R-3
R-4
S-1
S-2
OSPF 1
G0/0/0
G0/0/0
G0/0/1
G0/0/1
G0/0/0
G0/0/0
MPLS uses an existing IP network with information derived from a link-state protocol. Without this underlying IP network the MPLS process on the router does not have routes to assign MPLS labels to.

## Slide 5
G0/0/1
G0/0/1
R-1
R-2
R-3
R-4
MPLS BOUNDARY
G0/0/0
G0/0/0
G0/0/1
G0/0/1
G0/0/0
G0/0/0
MPLS boundaries can be different than OSPF boundaries. An OSPF domain can continue to extend past the last router running MPLS at any edge. MPLS labels are removed at that last “Label Edge Router” and traffic is simply routing beyond that point using standard OSPF and IP routing.
OSPF 1 AREA 0
Any devices running MPLS is a “Label Switched Router” (LSR) but devices that exist at the edge of an MPLS boundary are “Label Edge Routers” (LER)
LER
LER
LSR
LSR
R-6
R-5

## Slide 6: MPLS FORWARDING TABLE
LOCAL LABELS ARE ASSIGNED BY THE ROUTER LOCALLY. THIS IS THE LABEL THEY SHARE WITH THEIR MPLS NEIGHBORS TELLING THEM WHICH LABEL TO USE IF THEY NEIGHBOR IS SENDING TRAFFIC TOWARDS THIS ROUTER
OUTGOING LABELS ARE SHARED WITH THE ROUTER BY MPLS NEIGHBORS. THIS IS THE LABEL THAT SHOULD BE SENT TO THE NEIGHBOR SO THEY KNOW WHAT DESTINATION NETWORK YOU ARE TRYINTG TO REACH, IF THE LABEL SAYS “POP LABEL”, THAT MEANS THAT THIS ROUTER SHOULD REMOVE ANY MPLS LABELS BEFORE SENDING TO THE NEIGHBOR.
THE OUTGOING INTERFACE IS THE EXIT INTERFACE THAT THE PACKET SHOULD BE SENT TO
NEXT HOP IS THE IP ADDRESS OF THE MPLS NEIGHBOR THAT WILL BE REACHED VIA THE OUTGOING INTERFACE
THE PREFIX OR TUNNEL ID SHOWS THE SUBNET OR CIRCUIT ASSOCIATED WITH EACH LABEL.

## Slide 7
17.46.8.0 /24
G0/0/0
10.0.0.2
R-2
R-3
R-4
R-5
S-1
OSPF 1 AREA 0 - MPLS
G0/0/1
192.168.0.2
G0/0/1
G0/0/1
G0/0/0
G0/0/0
R1#
I WANT TO GET TO 17.46.8.0 /24 USING THIS MPLS NETWORK.
MY MPLS DATABASE SAYS MY LOCAL LABEL FOR THAT ROUTE IS “1001” SO THAT IS THE LABEL I GIVE TO MY MPLS NEIGHBORS IF THEY’RE USING ME TO GET TO 17.46.8.0 /24.
MY MPLS FORWARDING TABLE SAYS MY OUTGING LABEL FOR THAT ROUTE IS “2157” AND I SEND IT OUT MY G0/0/0 INTERFACE TO A NEXT HOP IP ADDRESS 10.0.0.2.
SO I PUT A LABEL OF “2157” ON
IT AND SEND IT OUT G0/0/0
R-1
G0/0/0
10.0.0.1
S-1
R-6
G0/0/0
1.1.1.6
G0/0/1
1.1.1.5
R2#
I RECEIVED AN MPLS PACKET FROM R1 MARKED WITH THE LABEL “2157”
MY MPLS DATABASE SAYS THAT’S MY LABEL FOR 17.46.8.0 /24.
MY MPLS FORWARDING TABLE SAYS MY OUTGOING LABEL FOR THAT ROUTE IS “3085” AND I SEND IT OUT MY G0/0/1 INTERFACE TO A NEXT HOP IP ADDRESS OF 192.168.0.3
SO I PUT A LABEL OF “3085” ON IT AND SEND IT OUT G0/0/1
G0/0/1
192.168.0.3
R5#
I RECEIVED AN MPLS PACKET FROM R4 MARKED WITH THE LABEL “5551”
MY MPLS DATABASE SAYS THAT’S MY LABEL FOR 17.46.8.0 /24.
MY MPLS FORWARDING TABLE SAYS MY OUTGOING INTERFACE IS G0/0/1 WITH A NEXT HOP OF 1.1.1.6, AND THAT THE NEXT ROUTER IS THE MPLS EDGE FOR THAT ROUTE.
SO I’M GOING TO POP THE LABEL OFF AND JUST SEND IT TO
OUT G0/0/1 AS IP.
R6#
I RECEIVED AN IP PACKET FROM R5 WITH A DESTINATION OF 17.46.8.100.
THAT NETWORK IS CONNECTED TO ME ACCORDING TO MY ROUTING TABLE SO I SEND THE PACKET OUT MY G0/0/2 INTERFACE.
G0/0/0
17.46.8.1

## Slide 8
Configuration
      R20(config)#ip cef
      R20(config)#mpls label protocol ldp
      R20(config)#mpls ldp router-id loopback0 force
      R20(config)#mpls label range 20000 20999
      R20(config)#mpls ip
      R20(config)#int g0/0
      R20(config-if)#mpls ip
Verification:
  Show mpls interface
  Show mpls ldp discovery
  Show mpls ldp neighbor
  Show mpls ldp bindings
  Show mpls forwarding-table
  Show mpls ip binding
  Show ip cef x.x.x.x
  Traceroute x.x.x.x (notice MPLS: Label XX in output)
MPLS Commands
Notes: ip cef
mpls label protocol [ ldp | tdp ]
mpls ip
***MPLS static label assignment or label ranges will not take effect until reload, or disable re-enable of mpls on interfaces***