## Slide 1: VRF BASICS

## Slide 2
R-1
R-2
G0/0/1
G0/0/2
G0/0/1
G0/0/2
11.0.0.0 /30
10.0.0.0 /30
R2#
Show ip route
C 10.0.0.0 /30 directly connected, G0/0/1
L 10.0.0.2 /32 directly connected, G0/0/1
C 11.0.0.0 /30 directly connected, G0/0/2
L 11.0.0.2 /32 directly connected, G0/0/1
R1#
Show ip route
C 10.0.0.0 /30 directly connected, G0/0/1
L 10.0.0.1 /32 directly connected, G0/0/1
C 11.0.0.0 /30 directly connected, G0/0/2
L 11.0.0.1 /32 directly connected, G0/0/2
VIRTUAL ROUTING AND FORWARDING (VRF) IS THE PROCESS OF CREATING MULTIPLE LOGICAL INSTANCES OF A ROUTER ON A SINGLE PIECE OF HARDWARE. SIMILARLY TO HOW A VLAN SEPERATES A SWITCH INTO TWO COMPLETELY SEGREGATED LOGICAL LAYER 2 NETWORKS, A VRF BREAKS A ROUTER INTO TWO SEPARATE LAYER 3 NETWORKS THAT ARE ISOLATED FROM EACH OTHER.
THAT MEANS TWO ROUTING TABLES AND TWO SETS OF DYNAMIC ROUTING PROCESSES THAT ARE NOT AWARE THEY ARE SHARING 1 PHYSICAL ROUTER.
BELOW IS AN EXAMPLE OF CONVENTION ROUTERS THAT ONLY HAVE A GLOBAL ROUTING TABLE.

## Slide 3
R-2
R-2
R-1
G0/0/1
G0/0/2
G0/0/1
G0/0/2
VRF XYZ
10.0.0.0 /30
11.0.0.0 /30
R2#
Vrf definition XYZ
address-family ipv4
address-family ipv6
Interface g0/0/2
vrf forwarding XYZ
ip address 11.0.0.2 255.255.255.252
Interface g0/0/1
ip address 10.0.0.2 255.255.255.252
ONCE A VRF IS DEFINED ON A ROUTER, THAT ROUTER ESSENTIALLY BECOMES TWO ROUTERS SHARING ONE SET OF PORTS, CPU AND OTHER PHYSICAL ASPECTS. UNDER THE VRF DEFINITION, LIST THE ADDRESS FAMILY THAT THE VRF WILL BE USED FOR (IPV4, IPV6 OR BOTH)
INTERFACES AND ROUTING PROTOCOLS/PROCESSES CAN BE ASSIGNED TO A VRF OR LEFT IN THE GLOBAL ROUTING TABLE.
IN THIS CASE R-2’S G0/0/2 INTERFACE IS ASSIGNED TO THE NEWLY CREATED VRF “XYZ”.

## Slide 4
R-2
R-2
R-1
G0/0/1
G0/0/2
G0/0/1
G0/0/2
VRF XYZ
10.0.0.0 /30
11.0.0.0 /30
VRF AWARE
VRF UNAWARE
R2#
Show ip route
C 10.0.0.0 /30 directly connected, G0/0/1
L 10.0.0.2 /32 directly connected, G0/0/1
R2#
Show ip route vrf XYZ
C 11.0.0.0 /30 directly connected, G0/0/2
L 11.0.0.2 /32 directly connected, G0/0/2
INTERFACES IN THE GLOBAL ROUTING TABLE CAN BE CONNECTED TO INTERFACES IN A VRF. NEITHER DEVICE KNOWS WHETHER THE ROUTER ON THE OTHER SIDE OF THE LINK IS IN A VRF. FROM R-1’S PERSPECTIVE, HE THINKS HE IS CONNECTEC TO TWO DIFFERENT ROUTERS SINCE THE ROUTING TABLE INFORMATION HE RECEIVES FROM THE R-2 GLOBAL WILL BE DIFFERENT THAT THAT HE RECEIVES FROM THE R-2 VRF.

## Slide 5
R-1
R-2
G0/0/1
G0/0/2
VRF XYZ
G0/0/1
G0/0/2
VRF XYZ
11.0.0.0 /30
10.0.0.0 /30
VRF AWARE
VRF AWARE
R2#
Show ip route vrf XYZ
C 11.0.0.0 /30 directly connected, G0/0/2
L 11.0.0.2 /32 directly connected, G0/0/1
R2#
Show ip route
C 10.0.0.0 /30 directly connected, G0/0/1
L 10.0.0.2 /32 directly connected, G0/0/1
R1#
Show ip route
C 10.0.0.0 /30 directly connected, G0/0/1
L 10.0.0.1 /32 directly connected, G0/0/1
R1#
Show ip route vrf XYZ
C 11.0.0.0 /30 directly connected, G0/0/1
L 11.0.0.1 /32 directly connected, G0/0/1
VRFs CAN BE EXTENDED ACROSS MULTIPLE ROUTERS AND MAINTAIN THEIR ISOLATED PATH. IN THIS CASE VRF XYZ HAS BEEN CREATED ON BOTH R-1 AND R-2 ALLOWING FOR TRAFFIC WITHIN THAT VRF TO STAY SEPARATE FROM THE GLOBAL ROUTING TABLES ON BOTH DEVICES. THIS COULD BE EXTENDED ACROSS MANY MORE ROUTERS.
NOTE: THE EASIEST WAY TO CONFIGURE MULTIPLE VRFs THAT SPAN SEVERAL ROUTERS IS TO USE EVN AND VNET TRUNKS.

## Slide 6
R-2
R-2
R-1
G0/0/1
G0/0/2
.1
G0/0/1
.2
G0/0/2
VRF XYZ
10.0.0.0 /30
11.0.0.0 /30
R2#
Router eigrp MSCHAT
Address-family ipv4 unicast vrf XYZ autonomous-system 10
Network 10.0.0.0 0.0.0.3
Network 12.1.0.0 0.0.0.255
Network 12.0.0.0 0.0.0.255
R2#
Show ip eigrp neighbor
Show ip eigrp vrf XYZ neighbor
0 10.0.0.1 G0/0/2 00:36…
R1#
Router eigrp 10
Network 10.0.0.0 0.0.0.3
Show ip eigrp neighbor
0 10.0.0.2 G0/0/2 00:36…
VRF AWARE
VRF UNAWARE
12.0.0.0 /24
12.1.0.0 /24
VRF XYZ
ROUTING PROTOCOLS AND STATIC ROUTES SUPPORT CONFIGURATION FOR VRFs AS WELL. WHEN A ROUTING PROTOCOL IS ASSIGNED TO A VRF, LIKE THE ONE TO THE RIGHT, THE DYNAMIC ROUTES IT LEARNS AND SHARES APPLY TO THAT VRF’S ROUTING TABLE RATHER THAN THE GLOBAL.

## Slide 7
R-1
R-2
G0/0/1
192.168.100.1
G0/0/1
172.26.150.1
VRF XYZ
R1#
Int g0/0/1
Ip add 192.168.100.1 255.255.255.0
Ip route 172.26.150.1 255.255.255.255 g0/0/1
Int tun 1
Ip add 1.1.1.1 255.255.255.252
Tunnel source 192.168.100.1
Tunnel destination 172.26.150.1
WAN
R1 AND R2 HAVE
BIDIRECTIONAL REACHABILITY
FROM THEIR G0/0/1 INTERFACES
INT TUN 1
1.1.1.1 /30
INT TUN 1
1.1.1.2 /30
VRF XYZ
R2#
Int g0/0/1
Vrf forwarding XYZ
Ip add 172.26.150.1 255.255.255.0
Ip route vrf XYZ 192.168.100.1 255.255.255.255 g0/0/1
Int tun 1
Vrf forwarding XYZ
Ip add 1.1.1.2 255.255.255.252
Tunnel destination 192.168.100.1
Tunnel source 172.26.150.1
Tunnel vrf XYZ
TUNNEL INTERFACES CAN ALSO UTILIZED VRFs FOR BOTH, TUNNEL UNDERLAY (SOUREC/DESTINATION) AND OVERLAY (TUNNEL INTERFACE).