## Slide 1: “Q-IN-Q TUNNELING”

## Slide 2
UNIT COLORLESS
(LAST LEG CIRCUIT)
X-1
X-2
S-2
S-3
S-4
INSTALLATION GAIT PoP
VLAN 10-15
VLAN 10-15
VLAN 10-15
VLAN 10-15
INSTALLATION NEC LAYER 2 NETWORK
VLAN 400-499
S-5
X-3
UNIT COLORLESS
(LAST LEG CIRCUIT)
VLAN 10-15
VLAN 10-15

## Slide 3
UNIT COLORLESS
(LAST LEG CIRCUIT)
X-1
X-2
S-2
S-3
S-4
INSTALLATION GAIT PoP
VLAN 10-15
VLAN 10-15
VLAN 10-15
VLAN 10-15
INSTALLATION NEC LAYER 2 NETWORK
VLAN 400-499
S-5
X-3
UNIT COLORLESS
(LAST LEG CIRCUIT)
VLAN 10-15
VLAN 10-15
X1#
!
Int g1/0/4
Sw mode trunk
Sw trunk allow vlan 10-15
X2#
!
Int g1/0/4
Sw mode trunk
Sw trunk allow vlan 10-15
G1/0/4
G1/0/4
X3#
!
Int g1/0/4
Sw mode trunk
Sw trunk allow vlan 10-15
G1/0/4
THE COLORLESS NETWORK IN THIS EXAMPLE IS THE “EXTERNAL” NETWORK

## Slide 4
UNIT COLORLESS
(LAST LEG CIRCUIT)
X-1
X-2
S-2
S-3
S-4
INSTALLATION
GAIT PoP
VLAN 10-15
VLAN 10-15
VLAN 10-15
VLAN 10-15
INSTALLATION NEC LAYER 2 NETWORK
VLAN 400-499
S-5
X-3
UNIT COLORLESS
(LAST LEG CIRCUIT)
VLAN 10-15
VLAN 10-15
S2#
!
Int g1/0/1
Sw mode dot1q-tunnel
Sw access vlan 499
G1/0/1
G1/0/1
G1/0/1
S5#
!
Int g1/0/1
Sw mode dot1q-tunnel
Sw access vlan 499
S4#
!
Int g1/0/1
Sw mode dot1q-tunnel
Sw access vlan 499
THE GREEN NETWORK IN THIS EXAMPLE IS THE “INTERNAL” NETWORK

## Slide 5
G1/0/10
SW MODE TRUNK
SW TRUNK ALLOW VLAN 5-6
VLAN 5
VLAN 6
G0/20
SW MODE DOT-1Q TUNNEL
SW ACCESS VLAN 100
G0/1
SW MODE TRUNK
SW TRUNK ALLOW VLAN 100
SW MODE TRUNK
SW TRUNK ALLOW VLAN 5-6
THE DEVICE ON NETWORK THAT IS PROVIDING THE TRANSPORT (IN THIS CASE, THE BROWN SWITCHES) IS THE ONE THAT HAS THE “DOT-1Q TUNNEL PORT” CONFIGURED ON THE PORT FACING THE EXTERNAL NETWORK (THE GREY SWITCHES).
THE DEVICE ON THE INTERNAL NETWORK THAT IS PROVIDING THE TRANSPORT (IN THIS CASE, THE BROWN SWITCHES) HAS A STANDARD TRUNK PORT CARRYING THE TRANSPORT VLAN (100) FACING THE OTHER DEVICES IN ITS OWN NETWORK.
THE DEVICE ON THE EXTERNAL NETWORK THAT IS BEING TRANSPORTED HAS A STANDARD TRUNK PORT WITH THE EXTERNAL VLANS ALLOWED, FACING THE DOT-1Q TUNNEL PORT ON THE INTERNAL NETWORK SWITCH.
EXTERNAL
INTERNAL