## Slide 1
ROUTER-PE#
VRF DEFINITION ABC  THE VRF FOR THE CUSTOMER IS DEFINED
ADDRESS-FAMILY IPV4  THE VRF IS ACTIVATED FOR THE CUSTOMER’S PROTOCOL (IPV4 OR IPV6)
RD 1:1  A ROUTE-DISTINGUISHER IS CONFIGURED WITHIN THE VRF IN ORDER TO IDENTIFY ROUTES FROM DIFFERENT VRFs WITHIN THE VPNv4 BGP TABLE
ROUTE-TARGET EXPORT 1:1  A ROUTE-TARGET IS CONFIGURED WITH THE “EXPORT” COMMAND FOR RD ROUTES THAT THE ROUTER WANTS TO SHARE WITH ITS IBGP VPNv4 PEERS
ROUTE-TARGET IMPORT 2:2  A ROUTE-TARGET IS CONFIGURED WITH THE “IMPORT” COMMAND FOR RD ROUTES THAT THE ROUTER WANTS TO LEARN FROM ITS IBGP VPNv4 PEERS
MPLS IP  ACTIVATES MPLS GLOBALLY ON THE ROUTER
MPLS LABEL PROTOCOL LDP  SPECIFIES THE LABEL PROTOCOL MPLS WILL USE
MPLS LABEL RANGE 10000 10999  SPECIFIES THE RANGE OF LABELS THAT THE ROUTER WILL ASSIGN TO PREFIXES IN ITS LOCAL LABEL DATABASE
MPLS LDP ROUTER-ID LOOPBACK 0 FORCE  DESIGNATED AN INTERFACE TO SERVES AT THE MPLS ROUTER-ID, THE WORD FORCE OVERRIDES A ROUTER-ID CHOSEN BY THE ROUTER
INT G0/0/1  AT LEAST ONE INTERFACE MUST BE PARTICIPATING IN MPLS, TYPICALLY FACING THE P ROUTER OR “CORE” ROUTER
MPLS IP  ACTIVATE MPLS ON THE INTERFACE
IP ADD 192.168.0.1 255.255.255.0
IP OSPF 1 AREA 0  MPLS WORKS BEST WITH LINK-STATE PROTOCOLS, THE MPLS NETWORK WILL LIKELY BE RUNNING A FAST IGP RATHER THAN RUNNING BGP WITHIN IT’S CORE
ROUTER EIGRP CUSTOMER_1  EIGRP NAMED MODE CAN SUPPORT VRF INSTANCES WHICH WORK WELL FOR SEPARATED CUSTOMERS. NOTE THAT THE ROUTER WOULD ALSO HAVE AN INTERFACE IN THIS VRF FACING THE CUSTOMER.
ADDRESS-FAMILY IPV4 UNI VRF ABC AUTONOMOUS-SYSTEM 1  SPECIFY THE VRF AND THE EIGRP AUTONOMOUS SYSTEM USED BY THE CUSTOMER
NETWORK 0.0.0.0  MORE SPECIFIC NETWORK STATEMENTS COULD BE USED HERE
TOPOLOGY BASE
REDISTRIBUTE BGP 65001  REDISTRIBUTION IS USED TO SEND ROUTES FROM THE VPNv4 BGP TABLE ON THE PE-ROUTER TO THE CUSTOMER VIA EIGRP
ROUTER BGP 65001
BGP ROUTER-ID 1.1.1.1
NEIGHBOR 10.0.0.2 REMOTE-AS 65001  THE VPNv4 BGP PEER ON THE OTHER SIDE OF THE MPLS NETWORK WILL BE CONFIGURED AS AN IBGP NEIGHBOR
ADDRESS-FAMILY VPNV4  CONFIGURE THE VPNv4 ADDRESS FAMILY
NEIGHBOR 10.0.0.2 ACTIVATE  ACTIVATE ANY IBGP PEERS THAT WILL PARTICIPATE IN THE L3 MPLS VPN
NEIGHBOR 10.0.0.2 SEND-COMMUNITY EXTENDED  THIS COMMAND POPULATES AUTOMATICALLY WHEN YOU ACTIVATE EACH PEER
ADDRESS-FAMILY IPV4 UNI VRF ABC  CONFIGURE AN ADDRESS FAMILY FOR THE VRF
REDISTRIBUTE EIGRP 1  PULL ROUTES INTO BGP FROM THE CUSTOMER’S VRF BY REDISTRIBUTING EIGRP