## Slide 1: NETWORK OPERATIONS PRACTICAL EXERCISES (NETWORK MANAGEMENT & NETWORK ENGINEERING)
STUDENT 13
SCENARIO: You have been deployed from Division staff to assist a subordinate tactical ops center that has been functioning without a network technician for an extended period of time. The network elements you have access to have some configuration left over from the previous technician’s attempts to administer the network.
You have access to a WAN Manager workstation in the S3 tent. From there you connect through a User Access Case switch and have remote access to the unit’s layer-3 switch and router. Segments of the network you are connected to has begun migration to IPV6 and your path back to the Division HQ requires utilization of an IPV6-only DMVPN and an IPV4-over-IPV6 GRE tunnel.
Your tasks will include:
Restoring network connectivity with higher headquarters
Establishing some basic SNMPc network management tools for the TOC
Implementing PACSTAR IQ-Core management resources
Setup and modification of some Net-Flow capabilities
Engineering solutions for problems with specific network reachability
Configuring simple automation to assist with local network issues
Improving network security features
**The diagram on the next page shows the end-state logical connectivity for your network when everything is working**

## Slide 2
STUDENT-13
WORKSTATION
STUDENT NETWORK:
22.18.113.0/29
VLAN 113
VM
OSTINATO
(MCS)
VM
MCS
.4
VM
PACSTAR
.2
VIRTUAL BOX
USER ACCESS
SWITCH
STUDENT-13
ROUTER
22.18.213.2
LOGIN: cisco
PASSWORD: cisco
STUDENT-1 L3 SWITCH
22.18.113.1
LOGIN: cisco
PASSWORD: cisco
VLAN 313
IPV6 ONLY
IPV6
WAN
TACTICAL
UPLINK
NODE 13
CORE
NODE 1
STRATEGIC
NODE
VLAN 413
OSPFV3 IPV6 DMVPN – TUN 59313
IPV4-OVER-IPV6 EIGRP – TUNNEL 113
MISSION
FILE SHARE
100.100.4.102
DOMAIN
CONTROLLER
100.100.4.101
GLOBAL NET
VLAN 213
TACT.
FW
STUDENT 13 LOGICAL DIAGRAM
IPV4
STRAT
STRATEGIC
FW
YOU HAVE TELNET AND/OR SSH
ACCESS TO THE STUDENT
WORKSTATION, VBOX VMs, STUDENT L3 SWITCH AND STUDENT ROUTER
Layer 2
NET
INT G0/0/0
INT G0/1
PC NIC
LINK TO UAC
SWITCH
PHYSICAL
CONNECTIVITY
STUDENT L3 SWITCH
STUDENT ROUTER
DIVISION
AGG.
ROUTER
USERNAME PASSWORD
STUDENT NETWORK DEVICES: cisco cisco
WAN-EDGE STUDENT LOGIN: student student
MCS VM: student CiscoLabs2018!!
PACSTAR VM: la-user !A@S3d4f5g6h7j8k
STUDENT PC WORKSTATIO: student CiscoLabs2018!!
MPLS MESH
STUDENT MPLS NODE

## Slide 3: PE 1 (task checklist)
CHECK | TASK | REMARKS
 | Log into your student workstation and verify that the PC has a DHCP lease in the 22.18.113.0/29 network | Student PC username/password: student / CiscoLabs2018!!
 | If you cannot obtain a DHCP IP address (attempt ipconfig release/renew), statically assign 22.18.113.3/29 | Default Gateway: 22.18.113.1
 | Verify that you can ping your Gateway: 22.18.113.1, which is Interface Vlan 113 on the student layer 3 switch | 
 | Open a putty session and access the student L3 switch at 22.17.1.13 via telnet or ssh | Username: cisco Password: cisco
 | Configure your student L3 switch to establish connectivity with your student router by creating INT VLAN 213 | INT VLAN 213, ip address: 22.18.213.1/29
 | Config OSPF process 13 area 13, activate VLAN 113 and 213 networks, set the VLAN 213 SVI as OSPF P2P | *configure OSPF passive-interfaces as necessary
 | Verify that you have formed an OSPF neighbor adjacency with your student router (show ip ospf neighbor) | **If not, troubleshoot until complete**
 | Verify that your L3 switch is configured as a DHCP server for VLAN 113, assigning 100.100.4.101 as the DNS | *make any necessary modifications*
 | Open a putty session and access the student router at 22.18.213.2 via telnet or ssh | Username: cisco Password: cisco
 | On the student L3 switch and router, configure logging to use your PC’s ip address and validate logging | Logging host 22.18.113.3 / **Use Tftp32 desktop app**
 | Configure timestamps service on student router and student L3 switch for logging with millisecond granularity | 
 | On the student router set time-zone and DST. Set the student router as a NTP stratum 2 source | (clock time-zone EST / clock summer-time EST recurring)
 | Config the switch to acquire NTP from the router and verify synchronization | *show ntp status*
 | Configure your student L3 switch as a SNMPv2 agent with a corresponding SNMPc device icon on your student PC | **configure separate Read-Only and Read-Write V2 access**
 | Configure your student L3 switch with snmp interface indexing persistent | 
 | Apply the existing “SNMP-VTY_ACL” (configured on your L3 switch) to the snmp v2 configuration | 
 | Configure an ICMP only icon on your SNMPc map for your student PC | 
 | Configure a point-to-point link icon between your PC and your L3 switch that polls based on ICMP reachability of the INT VLAN 113 address | 
 | Configure your student router as a SNMPv3 agent with a corresponding SNMPc device icon on your student PC | Authentication: SHA, Encryption: AES 128
 | In SNMPc, configure link monitoring between your router and L3 switch based on OSPF neighbor state | **use the MIB browser**

## Slide 4: PE 1 (task checklist)
CHECK | TASK | REMARKS
 | Verify that you have connectivity with the IPV6 WAN by pinging 2001:AA0D:AB02:AC02::2 | 
 | Configure a static default IPV6 route to 2001:AA0D:AB02:AC02::2 | 
 | Use the diagram below to derive all of the configs needed for your student router to be configured as a phase 3 DMVPN spoke in Tunnel 59313, OSPFv3 process 313 | *some specific IPV6 static routes have been pre-configured in the student router
IPV6
WAN
STUDENT
ROUTER
UPLINK
NODE
13
TUNNEL IP: FC00::113:A002/122
TUNNEL SOURCE: 2001:AA0D:AB02:AC02::1
OSPFV3 PRIORITY: 0
IPV6 NHRP SHORTCUT
** SEE TEMPLATE ON LAST PAGE FOR EXAMPLE **
TUNNEL IPV6 ADDRESS: FC00::113:A001/122
TUNNEL SOURCE: 2001:E42C:23AB:F00D::2139
IPV6 MTU: 1392
NHRP AUTHENTICATION: n3tm@n19
NHRP NETWORK ID: 11159313
TUNNEL KEY: 20191223
TUNNEL MODE: GRE MULTIPOINT IPV6
OSPFV3 313 IPV6 AREA 13
OSPFV3 NETWORK TYPE: POINT-TO-MULTIPOINT
OSPFV3 COST: 2600
OSPFV3 FLOOD-REDUCTION
OSPFV3 HELLO-INTERVAL: 10 SEC
OSPFV3 DEAD-INTERVAL: 40 SEC
IPV6 ENABLE
IPV6 PIM
CHECK | TASK | REMARKS
 | Verify that you have obtained an IPV6 neighbor adjacency with the uplink node | Show ospfv3 neighbor
 | Verify that you are receiving dynamic routes from the IPV6 WAN | Show IPV6 route

## Slide 5: PE 2 (task checklist)
CHECK | TASK | REMARKS
 | Once your underlying IPV6 connectivity is established via Tunnel 59313, use the diagram above to derive all of the configs needed on your student router to build a 4-over-6 tunnel to the Core router and establish an EIGRP neighbor for mission command traffic. | *EIGRP will not establish without authentication, see tasks below
 | Configure a key chain called NETMAN and assign key 1 the key-string 31GRpK3y | Apply the key-chain to the EIGRP config and specify MD5 mode
 | Verify an EIGRP neighbor adjacency has been established between your student router and the core router | Show ip eigrp neighbor
 | Configure IPV4 mutual redistribution on the student router between the OSPFv2 (process 13) and EIGRP 113 | 
 | Verify dynamic routes (to include a default route) are being learned by your student router via EIGRP | Show ip route eigrp
 | Verify that your student L3 switch is learning eigrp routes by way of redistribution from the router (into OSPFv2) | Show ip route ospf
 | Verify ICMP reachability to the Division file share server and Domain Controller from the student PC | Ping 100.100.4.102 / 100.100.4.101 (sourced from 22.18.113.3)
 | In SNMPc, configure link monitoring on your student router for ICMP reachability of the IPV4 next-hop address | *172.30.13.2
 | In SNMPc, configure link monitoring between your student router and the core router based on EIGRP state | SEE THE PE-3 RESOURCE FOLDER FOR CONFIG HELP
 | On your student router configure ip sla operation: dns-lookup sla for labtech.netmanlab.local, frequency 10 | Reference DNS: 100.100.4.101
 | On your student router configure ip sla operation: icmp-echo to 172.30.113.2, frequency 5 | 
 | On your student router configure ip sla op: icmp-jitter to 22.17.17.1, frequency 5 | 
 | On your student router configure ipv6 sla op: icmp-echo to 2001:BAD:C0DE:D234::1 source-int G0/0/0.313 | 
 | Access the Division file share server at 100.100.4.102 and copy the folder “NETMAN PE-3 resources” to your PC | 
STUDENT
ROUTER
UPLINK
NODE
13
TUNNEL IP: 172.30.13.1 255.255.255.252
TUNNEL SOURCE: 2001:CE33:C113:1000::1
TUNNEL MODE: GRE IPV6
TUNNEL KEY: 8675313
MTU: 1392
TCP MAX SEGMENT SIZE: 1360
TUN 59313
*ESTABLISHED IPV6 OSPF*
TUN 113
4-OVER-6 (EIGRP)
TUNNEL IP: 172.30.13.2 255.255.255.252
TUNNEL SOURCE: 2001:CE33:C254:1E01::FFD
TUNNEL MODE: GRE IPV6
TUNNEL KEY: 8675313
CORE
NODE
EIGRP PROCESS: STDN13
ADDRESS FAMILY: IPV4
AUTONOMOUS SYSTEM: 113
*ACTIVATE THE TUNNEL
NETWORK IN EIGRP

## Slide 6: PE 3 (task checklist)
CHECK | TASK | REMARKS
 | Configure your student router with the archive capability | SEE THE PE-3 RESOURCE FOLDER FOR CONFIG HELP
 | Configure an emergency login account | SEE THE PE-3 RESOURCE FOLDER FOR CONFIG HELP
 | Configure secure copy capability on your router | ip scp server enable
 | Ensure the student router IOS image in use conforms to the Division standard | SEE THE PE-3 RESOURCE FOLDER FOR CONFIG HELP
 | What is the MD5 hash value from the student router IOS file: Does it match the expected hash value? | Value:______________________________ YES / NO
 | Create a 2-character alias command for viewing the eigrp configuration running on your student router | SEE THE PE-3 RESOURCE FOLDER FOR CONFIG HELP
 | Create a 2-character alias command to enter configuration mode for router ospf process 13 | 
 | Turn on your PACSTAR VM in virtual box. Access using the credentials provided: | Username: lab-user Password: !A@S3d4f5g6h7j8k
 | Ensure your PACSTAR VM is statically assigned the IP address: 22.18.113.2/29 Gateway: 22.18.113.1 | 
 | Configure basic monitoring icons and connectivity links for your student PC and network devices in IQ-Core | SEE THE IQ-CORE PDF GUIDE IN THE PE-3 RESOURCE FOLDER
 | Configure link monitoring in IQ-Core for the OSPF neighbor state between the L3 switch and the student router | 
 | Create an script in IQ-Core that configures IPSEC on your student router based on the Division IPSEC cut-sheet | SEE THE PE-3 RESOURCE FOLDER FOR CONFIG HELP *some IPSEC features (key/address) are configured later in the PE*
 | Utilizing IQ Core, create an initial Backup of both switch and router. Once complete, add detailed descriptions to all used and unused interfaces and Create a second Backup. Use the Compare feature to verify the differences between to two configurations. | SEE THE IQ-CORE PDF GUIDE IN THE PE-3 RESOURCE FOLDER

## Slide 7: PE 3 (task checklist)
CRYPTO ISAKMP KEY: netmanistan
ADDRESS: 2001:E42C:23AB:F00D::2139/128
CHECK | TASK | REMARKS
 | IPSEC has been implemented on the uplink node for the IPV6 DMVPN. Use the information above (combined with the IPSEC configuration scripted into the Student router from IQ-Core) to bring Tunnel 59313 back online. | If the IPSEC configuration was not effectively applied using IQ-Core, configure it manually using the DIV IPSEC cut-sheet
 | Apply the profile to the IPV6 DMVPN tunnel and ensure all IPV6 and IPV4 connectivity has been restored | Tunnel protection ipsec profile [profile name]
 | Telnet from your student terminal to the NETMAN Proving Grounds Node at 22.17.17.28 | Username: student Password: student
 | Within the router, determine the next-hop IP address for the 148.75.1.0 network | Next-hop via (IP): ___________________________________
 | Within the router, determine description configured for the G0/0/0.39 sub-interface | Description: _________________________________
 | Configure a menu capability on your student router wherein a designated user can ONLY perform: 1) show current ospf neighbors 2) show current eigrp neighbors 3) exit from the device | SEE THE PE-3 RESOURCE FOLDER FOR CONFIG HELP
 | Login to the student router with the menu-only credentials and test the functionality | *Remove application of the menu from the VTY lines after you have tested it*
 | Configure flexible Net-Flow on your student router (flow record / flow exporter / flow monitor) | SEE THE PE-3 RESOURCE FOLDER FOR CONFIG HELP
 | Map your flow monitor to your Tunnel 113 interface and monitor input and output traffic | 
 | Run a flow capture and determine which transport source port is being used by 100.100.4.101 (show flow monitor [NAME] cache) *You can use the pipe “¦” command to filter results | TRNS SOURCE PORT #________________
 | Turn on your MCS VM in Virtual Box | 
 | Configure your student router as a monitored node via SNMPv3 on your Orion MCS server | SEE THE PE-3 RESOURCE FOLDER FOR CONFIG HELP
 | Configure your student workstation as a monitored node on your Orion MCS server using “Status Only: ICMP” | 
 | Configure the SLAs from Day 1 in your Orion MCS server | SEE THE PE-3 RESOURCE FOLDER FOR CONFIG HELP
 | Redirect syslog messages from the student router to your Orion MCS server | Logging host 22.18.113.4
LAB UPDATE:
DO NOT APPLY THE IPSEC TO YOUR TUNNEL AS INDICATED IN THE SECOND TASK (BELOW). VERIFY THAT THE CONFIGURATION WAS IMPORTED FROM THE IQ-CORE SCRIPT AND COMPLETE THE CONFIGURATION USING THE CRYPTO KEY (RIGHT) BUT DO NOT CONFIGURE TUNNEL PROTECTION ON YOUR DMVPN AT THIS TIME.

## Slide 8: PE 4 (task checklist)
CHECK | TASK | REMARKS
 | Your higher headquarters wants to be able to pass traffic between your new IQ-Core server on the Student LAN and several operational servers and devices on the global network. However, traffic sourced from the 22.18.113.2 has been blocked by a tactical FW in the path. You can’t change the IP address of the IQ-Core server but Division has coordinated a PPS that will allow that one IP address to traverse the local strategic network. | 
 | Use the diagram below to configure a VLAN 413 sub-interface on the student router. | 
 | Ensure you have ICMP reachability to the VLAN 413 interface on the strategic node sourced from 10.41.3.254. | 
CHECK | TASK | REMARKS
 | Traffic sourced from 22.18.113.2 has to be able to reach several unspecified global addresses not included in the student network routing table, but the rest of the student router traffic cannot be impacted. Use police based routing to send all traffic received on the student router sourced from 22.18.113.2 directly to the strategic node as it’s IP next hop. After implementing the PBR, verify that the IQ-Core server is able to reach 100.100.4.101 and 206.154.33.232 | 
STUDENT
ROUTER
UPLINK
NODE
13
TUN 59313
*ESTABLISHED IPV6 OSPF*
TUN 113
4-OVER-6 (EIGRP)
CORE
NODE
TACT.
FW
STRAT
FW
STRAT NODE
GLOBAL NET
G0/0/0.413
10.41.3.254/29
G0/0/0.413
10.41.3.253/29
BLOCKING
22.18.113.2
PERMITTING
22.18.113.2
STUDENT LAN

## Slide 9: PE 5 (task checklist)
CHECK | TASK | REMARKS
 | Due to recent bandwidth consumption analysis based on unnecessary traffic, you need to configure an automated process on your student router that only allows traffic destined for your MCS to traverse the student LAN network when the MCS VM is online and the PACSTAR VM is not. | 
 | On the student router, configure two IP SLAs that check for reachability of the MCS and PACSTAR VMs separately with frequencies of 5 seconds. | SEE THE PE-3 RESOURCE FOLDER FOR CONFIG HELP
 | On the student router, configure two tracks that monitor the state of the two SLAs. | SEE THE PE-3 RESOURCE FOLDER FOR CONFIG HELP
 | On the student router, configure a third track as a Boolean list that is only in an UP state if the MCS track is UP and the PACSTAR track is down. | SEE THE PE-3 RESOURCE FOLDER FOR CONFIG HELP
 | On the student router configure an extended ACL that denies traffic destined for the MCS’s IP address and apply it to interface Tunnel 113 inbound. | 
 | On the student router configure an event manager applet to automatically remove the extended ACL from Tunnel 113 if the state of the 3rd track is UP. | SEE THE PE-3 RESOURCE FOLDER FOR CONFIG HELP
 | On the student router configure a second event manager applet to automatically re-apply the extended ACL to Tunnel 113 if the state of the 3rd track is DOWN. | 
 | With the MCS powered down and the PACSTAR VM online, use the command “show track” to ensure that track 3 state is down. | 
 | Verify that your configuration is working by turning on the MCS VM while the PACSTAR VM is still online. The track 3 state should still be DOWN because of the “AND” aspect of it’s Boolean list. | 
 | Verify that your configuration is working by disabling the PACSTAR VM NIC with the MCS still online. The track 3 state should now be UP. | 
 | Verify that your event manager automation worked correctly by showing the running configuration of interface Tunnel 113. The extended ACL should have been automatically removed when the track state of object 3 changed to UP. | 
 | Disable the MCS NIC or re-enable the PACSTAR VM NIC and ensure that the extended ACL is automatically re-applied as the state of object 3 changes back to DOWN. | **When testing is complete turn off the MCS VM completely

## Slide 10: PE 6 (task checklist) - For PE 6, Identify another student and notify the instructor of the student numbers for your “battle buddy team”.
 | TASK | REMARKS
 | You have been tasked with informally monitoring some LAN devices for another organization for a few days. Due to network policy, the path for this traffic must be entirely isolated within the student router. | 
 | A dedicated circuit has been established for a connection between you and the other student network on student router sub-interface G0/0/0.X. Establish a VRF path on your router per the diagram below so that the student network can be extended to your student L3 switch and reachable from your SNMPc server (student PC). | *The instructor will provide you the value of “X” for this lab.* VRF DEFINTION NET-A ADDRESS-FAMILY IPV4 UNICAST
 | On your router, config a host route making your tunnel destination reachable with the neighbor as the next-hop via G0/1 On your router, config a host route making your tunnel source on the L3 switch reachable from the router VRF. On your L3 switch, config a host route to the tunnel destination with your router’s VRF interface as the next hop | R# IP ROUTE VRF NET-A 22.17.1.B 255.255.255.255 10.0.0.B R# IP ROUTE VRF NET-A 22.17.1.13 255.255.255.255 10.99.13.253 S# IP ROUTE 22.17.1.B 255.255.255.255 10.99.13.254
 | Ensure you create VLAN 613 on your L3 switch and allow it to trunk across G1/0/1 to your student router. | First read “Allow VLAN Trunks” in the Resource Folder
 | Establish a tunnel and an EIGRP 100 neighbor across the connection between your student router and the neighboring node. Activate the tunnel network and the student LAN (22.18.113.0/29) network in EIGRP 100. | 
 | Once the EIGRP neighbor is established, verify that the neighbor LAN route is in your student L3 switch and add your neighbor’s SNMPc map as a monitored domain | SEE THE PE-3 RESOURCE FOLDER FOR CONFIG HELP
 | Validate than none of the routes associated with the path appear in the routing table. | Show ip route
G0/0/0.613
VRF FORWARDING NET-A
10.99.13.254/30
INT VLAN 613
10.99.13.253/30
INT G0/0/0.X
VRF FORWARDING NET-A
10.0.0.13/27
INT G0/0/0.X
INT TUN 600
10.60.0.0/24
EIGRP 100
.13
.B
INT TUN 600
IP ADD 10.60.0.13 255.255.255.0
TUNNEL SOURCE 22.17.1.13
TUNNEL DESTINATION 22.17.1.B
IP ROUTE 22.17.1.B 255.255.255.255 10.99.13.254
STUDENT ROUTER A
(VRF AWARE)
STUDENT ROUTER B
(VRF AWARE)
STUDENT L3 SWITCH B
(VRF UNAWARE)
STUDENT L3 SWITCH B
(VRF UNAWARE)
STUDENT PC B
STUDENT PC A
YOU ARE STUDENT A ON YOUR DIAGRAM.
USE THE DIAGRAM TO THE RIGHT BY REPLACING “B” WITH YOUR NEIGHBOR STUDENT’S NUMBER. THEY WILL NEED TO DO THE SAME ON THEIR CONFIGURATION, REPLACING THE “B” ON THEIR DIAGRAM WITH YOUR CONFIGURATION/STUDENT NUMBER.

## Slide 11: PE 7 (task checklist)
 | TASK | REMARKS
 | You have been tasked with building a eBGP neighbor with a mission partner (RCMP) that does not allow IGPs for customer connections. Configure a new sub-interface for VLAN 513 on your G0/0/0 interface per the diagram below. | Verify that it is operational by pinging 22.19.63.27.
 | Configure a static host route from your student router for the RCMP loopback 13 interface on the diagram. Use your new sub-interface as the exit interface or use the .27 as the next hop IP. | Ip route 22.19.129.13 255.255.255.255 g0/0/0.513 or Ip route 22.19.129.13 255.255.255.255 22.19.63.27
 | Per the diagram, configure loopback 1 on your student router. | 
 | Once you can ping the destination RCMP node, config an eBGP peer with the loopback 13 IP address as your neighbor for autonomous system 65421. You will have to use ebgp multihop set for at least 3. | SEE THE PE RESOURCE FOLDER FOR CONFIG HELP
 | Set the update source as loopback 1 for your eBGP neighbor. | SEE THE PE RESOURCE FOLDER FOR CONFIG HELP
 | Advertise your student LAN network (vlan 113) in your BGP process. | SEE THE PE RESOURCE FOLDER FOR CONFIG HELP
 | You should be learning a BGP route from the RCMP node that allows ICMP reachability of the TAC Portal Server. | 
 | Redistribute BGP from your student router into your Layer 3 switch. Ensure you see the TAC Portal Server network in your L3 switch as an “O E2” route. | SEE THE PE RESOURCE FOLDER FOR CONFIG HELP
 | Use TFTP on your student L3 switch to import a file to your flash from the TAC Portal Server. File name: ps-13-modelo.text | SEE THE PE RESOURCE FOLDER FOR CONFIG HELP
 | From your PC extract the modelo file from your switch using TFTP. You will need the access code for future use (PE 10). | 
 | Once you have the file on your student PC, delete it from the flash on your layer 3 switch. | Delete flash:ps-13-modelo.text
INTG0/0/0.513
22.19.63.1 /27
STUDENT ROUTER
BGP ROUTER-ID 22.19.0.13
BGP 65413
INT Lo 1
22.19.0.13 /32
RCMP
BGP ROUTER-ID 22.16.231.1
BGP 65421
TAC Portal Server
22.16.231.90
INT Lo 13
22.19.129.13 /32
RCMP WAN
Before you begin PE 7, set your L3 switch TFTP source to your Student LAN interface (int vlan 1xx)

## Slide 12: PE 8 (task checklist)
CHECK | TASK | REMARKS
 | You have been tasked with obtaining access to a mission command server that is located in different region. Connectivity traverses an MPLS backbone and access has been coordinated for you to engineer a transport link from your student router. To ensure the MPLS network does not introduce any problematic routes into your network you will setup the link within a VRF. | 
 | Designate the VRF your created in lab 6 (NET-A) for both address families ipv4 and ipv6. | 
 | Enable the G0/0/1 interface on your student router and assign it to the NET-A VRF. Configure it with the ipv4 address specified below on the diagram and assign an IPv6 link local address. Create Loopback 10 as depicted in the diagram below and also assign it to the VRF. | 
 | Configure ospfv3 process 1000 area 25 for the VRF and activate Loopback 10 and G0/0/1 in that process by specifying ospfv3 1000 ipv4 area 25 on the interfaces. | OSPFv3 network type will be broadcast (which is the default).
 | Verify that you have formed at least one OSPFv3 neighbor within the VRF process and check to see if you are learning the route to the mission command server. | Show ospfv3 vrf NET-A neighbor Show ip route vrf NET-A ospfv3
MPLS
BACKBONE
STUDENT
ROUTER
DISTANT END
NODE
INT G0/0/1
VRF forwarding NET-A
14.197.221.143 /24
CHECK | TASK | REMARKS
 | Activate MPLS on your student router and assign a label range of 51301 to 51399. Specify the mpls label protocol as LDP and force your student router to use loopback 10 as the mpls router-id. | SEE THE PE-3 RESOURCE FOLDER FOR CONFIG HELP
 | What label is assigned as the outgoing label for the 14.191.154.0/24 network? | Show mpls forwarding table LABEL ______________________________
 | What TCP port number is associated with your LDP peer? (show mpls ldp neighbor vrf NET-A) | TCP Port Number for Connection: _____________________
MISSION
COMMAND
SERVER
14.193.240.0
INT Loopback 10
VRF forwarding NET-A
22.18.13.10 /32

## Slide 13: PE 9 (task checklist)
 | TASK | REMARKS
 | You have been tasked with obtaining access to an MPLS node at another location in order to provide config and engineering support. In order to access the node you must first make some config changes to your student router and layer 3 switch. | 
 | Log into your student router and check the VRF NET-A routing table for an OSPFv3 route 22.20.43.0 /29. | Show ip route vrf NET-A.
 | If the route is not in your VRF routing table, ensure you have the VRF NET-A OPSFv3 neighbor you obtained in PE-8. | Let instructor know if there are any problems
 | You need to share a route for the student LAN into the OPSFv3 network but you cannot use basic redistribution because the student LAN is part of your router’s global routing table and the OSPFv3 network is within VRF NET-A. Configure a standard ACL (use your student number as the ACL number) with a permit statement matching your student LAN. | 
 | On your student router, configure a route-map called “MXO” that matches the ACL you configured in the last step. | 
 | On your student router under the ipv4 address-family config for VRF NET-A definition, use route-replication to pull the student LAN route from global routing table into the VRF routing table. View VRF NET-A routing table to verify the route is replicated ( + mark). | route-replicate from vrf global unicast ospf 13 route-map MXO
 | In some scenarios, route-replication can be used in conjunction with redistribution between VRFs. For this PE you will also configure a static route for VRF NET-A on your student router for your student LAN with the L3 switch VLAN 613 IP as the next-hop. | Ip route vrf NET-A 22.18.113.0 255.255.255.248 10.99.13.253 NOTE: The AD of this static route will cause this route to replace the replicated route in the VRF routing table.
 | Go into your OSPFv3 1000 process for address-family IPv4 vrf NET-A and redistribute static with the MXO route-map applied. | 
 | On your student router, config a VRF NET-A static route to your student LAN with the L3 switch’s VLAN 613 IP as the next-hop. | Ip route vrf NET-A 22.18.113.0 255.255.255.248 10.99.13.253
 | On your L3 switch config a static route to the MPLS node subnet (22.20.43.0 /29) with the router G0/0/0.613 IP as the next-hop. | 
 | Attempt to ping the student MPLS node below based on the IP in the diagram. SSH into the MPLS device. | Username: cisco Password: cisco
OSPFv3 1000
STUDENT
ROUTER
STUDENT PC
22.18.113.3
INT G0/0/1
VRF FORW NET-A
14.197.221.143 /24
MPLS
NETWORK
STUDENT
L3 SWITCH
(VRF UNAWARE)
STUDENT
MPLS NODE
22.20.43.6 /29
INT G0/0/.613
VRF FORW NET-A
10.99.13.254 /30
INT VLAN 613
10.99.13.253 /30
STUDENT LAN
22.18.113.0 /29

## Slide 14: PE 10 (task checklist)
 | TASK | REMARKS
 | Now that you have obtained access to your MPLS node, you have been tasked with engineering connectivity for a server that has been relocated. The Ostinato server used to reside on your student LAN but it had to be moved to the East Data Center. The server must keep its original IP address (22.18.113.5) and be able to reach it’s gateway (22.18.113.1) on the student LAN. | 
 | A pair of contracted layer 2 segments has been put in place between your student layer 3 switch and your MPLS node. Enable port G0/2 on your L3 switch and verify that the MPLS node’s G1/0/2 port is connected by using the command “show cdp neighbor”. | A pseudowire interface is a routed port. Before you config G1/0/2 as xconnect, you must convert it to a layer 3 port.
 | You need to configure a pseudowire link allowing your student LAN to be connected to vlan 113 on the East Data Center Distro Switch. Create BGP process 65222 on your MPLS node and configure your BGP router-id as 22.20.0.13. | 
 | Configure an iBGP neighbor based on the Eastern Edge Node G1/6 interface and configure the neighbor with next-hop-self. | The neighbor BGP password is the code from the modelo file.
 | On your MPLS node verify that you have a bgp neighbor with the command show ip bgp summary. | Troubleshoot as necessary until a bgp neighbor is established.
 | On your MPLS node create a pseudowire class called “PW-S13” and set it for mpls encapsulation. | 
 | Config your MPLS node G1/0/2 interface as a pseudowire xconnect with the Eastern Edge node’s BGP router-id and a circuit number 113. Designate the xconnect interface as encapsulation mpls and reference the pseudowire class you created. | See PE resource guide for configuration help
 | Verify that your pseudowire is operational by running the command “show cdp neighbor” on your student layer 3 switch. It should now appear as though you are directly connected to the East Data Center Distro Switch. | 
 | Verify the path between your student LAN and the Ostinato server by pinging it from your student PC and VLAN 113 SVI. | 
OSPFv3 1000
STUDENT
ROUTER
STUDENT PC
22.18.113.3
EASTERN
EDGE NODE
BGP AS 65222
BGP ROUTER-ID 22.20.0.99
STUDENT
L3 SWITCH
STUDENT
MPLS NODE
22.20.43.6 /29
STUDENT LAN
22.18.113.0 /29
MPLS
NETWORK
OSTINATO
SERVER
22.18.113.5 /29
EAST DATA-CENTER
DISTRO SWITCH
22.18.113.5 /29
iBGP LINK
LAYER 2 PATH
G1/0/2
G1/6
22.20.254.253
G0/2
TRUNK

## Slide 15: PE 11 (task checklist) Identify another student and notify the instructor of the student numbers for your “battle buddy team” – You can also use the same partner and same VLAN you used for PE 6.
 | TASK | REMARKS
 | You are planning to merge some network resources with another site and will need to share 2 common VLANs with another organization. You want to keep the path layer 2 and the other unit is not collocated. Your MPLS switch has a physical link to theirs but the VLANs that will be implemented (VLAN 750 and 760) cannot be added to the MPLS switch database. You have been tasked with testing a Q-in-Q layer 2 tunneling concept with the other unit. | 
 | Configure VLAN 750 and 760 on your student layer 3 switch and configure SVIs according to the diagram. These will serve as your test endpoints. The organization you are partnering with will do the same but they will use their student number as the last octet. | 
 | Enable interface G0/3 on your student layer 3 switch and configure it as a trunk that allows VLANs 750 and 760. | 
 | Enable interface G1/0/3 on your MPLS node and configure it as a dot1q-tunnel interface with access VLAN X. | 
 | Enable interface G1/0/24 on your MPLS node and configure it as a trunk allowing VLAN X. | 
 | This should complete the Q-in-Q path between your layer 3 switches. Verify that VLANs 750 and 760 do NOT exist in the MPLS node VLAN database(s) and VLAN X does not exist on the layer 3 switches. | 
 | Test the Q-in-Q tunnel by pinging from the VLAN 750 and 760 SVIs to the respective partner node SVIs. | 
STUDENT
L3 SWITCH
STUDENT
MPLS NODE
G0/3
G1/0/3
PARTNER
MPLS NODE
PARTNER
L3 SWITCH
G1/0/24
G1/0/24
TRUNK ALLOW
VLAN X
INT VLAN 750
10.75.0.a /24
INT VLAN 760
10.76.0.a /24
INT VLAN 750
10.75.0.b /24
INT VLAN 760
10.76.0.b /24
TRUNK
VLAN ALLOW
750, 760
TRUNK
VLAN ALLOW
750, 760
b = partner’s student number
DOT1Q TUNNEL PORT
ACCESS VLAN X
DOT1Q TUNNEL PORT
ACCESS VLAN X
a = your student number
X = instructor assigned VLAN
(or same as used in PE6)

## Slide 16: PE 12 (task checklist)
 | TASK | REMARKS
 | You have been tasked to engineer connectity with a mission endpoint network that is participating in an exercise. You need to be build a small network enclave on your layer 3 switch and configure a layer 3 MPLS VPN on your MPLS node in order to import and export routes with the mission endpoint. | On your L3 switch, configure loopback 113 and the G0/4 interface according to the diagram. The L3 switch is entirely VRF unaware.
 | The exercise network uses RIP version 2 as a routing protocol. Enable RIP on your L3 switch and activate the loopback 113 network and the G0/4 interface only. Configure RIP so that it does not summarize classful networks automatically. | See PE resource guide for help.
 | On your student MPLS node, configure a VRF called TWO-13 and activate is for address-family IPv4. | Assign RD (route distinguisher) 100:13 to the VRF.
 | Configure your MPLS node G1/0/4 interface and assign it to VRF TWO-13. | 
 | Configure RIP version 2 on your MPLS node for address-family ipv4 VRF TWO-13. Activate theG1/0/4 network, set no auto-summary. When complete, check the vrf routing table on your MPLS node to ensure you are receiving R routes from your L3 switch. | See PE resource guide for help.
 | In order to import and export routes with the distant end MPLS VPN node, you will need to first establish an iBGP peer in autonomous system 65222. Configure the BGP neighbor statement based on the IP address in the diagram and assign an update source of loopback 0. Verify you have a BGP peer with the command “show ip bgp summary”. | 
 | On your MPLS node, configure the BGP VPNv4 address-family and activate the MPLS VPN NODE neighbor. | Address-family vpnv4 Neighbor 14.195.8.0 activate
 | On your MPLS node, configure an IPv4 BGP address-family for your VRF and redistribute your RIP routes into BGP w/ a metric of 5. | See PE resource guide for help.
 | On your MPLS node, configure route targets within your VRF to import the distant end RD (0:13) and export your RD (100:13) | See PE resource guide for help.
 | You should now see routes from the distant end populated in your BGP VPNv4 table. | Show bgp vpnv4 unicast vrf TWO-13
 | Lastly, redistribute the BGP 65222 routes into the RIP process on your MPLS node, use a metric of 6. Check the global routing table on your layer 3 switch to ensure you are learning the two R routes from the exercise mission endpoint enclave in the diagram. | 
STUDENT
L3 SWITCH
STUDENT
MPLS NODE
G0/4
(VRF UNWARE)
G1/0/4
VRF TWO-13
(VRF AWARE)
G1/0/1
Loopback 113
172.26.13.1/32
iBGP PEER AS 65222
DISTANT END
MPLS VPN NODE
EXERCISE
MISSION
ENDPOINT
MPLS
172.27.13.1 /32
172.27.213.0 /30
RIP NETWORK VRF
RD 0:13
14.195.8.0
RIP
VRF TWO-13
RD 100:13
172.26.213.0 /30
.1
.2

## Slide 17: NETWORK OPERATIONS PRACTICAL EXERCISES LAB COMPLETION
STUDENT 13
1) RUN THE COMMAND “RESET” FROM PRIV EXEC MODE ON THE L3 SWITCH
PASSWORD: 123456789
2) RUN THE COMMAND “RESET” FROM PRIV EXEC MODE ON THE STUDENT ROUTER
PASSWORD: 123456789
REMOVE ALL FILES FROM THE DESKTOP EXCEPT FOR THE FOLDER MARKED 2020-NM AND THE LAB-PE PDF
(IF YOU ADDED NEW FILES TO THAT FOLDER, PLEASE DELETE THEM)
CLICK FILE > RESET ON THE SNMPc APPLICATION ON THE STUDENT PC
REMOVE CONFIGURATION FROM THE PACSTAR IQ-CORE MANAGEMENT SOFTWARE
POWER DOWN THE PACSTAR VM

## Slide 18
VM
OSTINATO
(MCS)
VM
MCS
VM
PACSTAR
(WIN7)
VIRTUAL BOX
INTERNET
STUDENT
PC
VIRTUAL
MACHINES
RUNNING
ON PC
CLASSROOM
SWITCH
CORE SWITCH
STUDENT SWITCH
FARM SWITCH
STUDENT ROUTER
FARM SWITCH
MPLS GATEWAY
MPLS MESH
INSTRUCTOR
DEVICE
AGGREGATE SWITCH
EXAM NODE
DATA CENTER
ROUTER
LAB DATA CENTER
TACTICAL UPLINK
NODES
TACTICAL CORE
NODES
WAN
EDGE
NODE
BGP LAB
NODE
STUDENT
MPLS
NODE
STUDENT
ROUTER
STUDENT
L3 SWITCH
STUDENT PHYSICAL DIAGRAM
(ACTUAL LAB CONNECTIVITY)
STUDENT PCs ARE PHYSICALLY CONNECTED TO SIX LAYER 2 “CLASSROOM” SWITCHES THAT ARE UNDER THE TABLES AND DESKS.
THE CLASSROOM SWITCHES TRUNK THE STUDENT VLANs BACK TO A SINGLE CORE SWITCH.
THE CORE SWITCH TRUNKS TRAFFIC TO A STUDENT SWITCH “FARM SWITCH” THAT HAS DIRECT PHYSCIALLY LINKS TO EACH STUDENT LAYER 3 SWITCH RACK-MOUNTED IN THE BACK OF THE CLASSROOM. THE LAYER 2 PATH FROM STUDENT PC TO STUDENT L3 SWITCH MAKES THE SWITCHES IN THE PATH TRANSPARENT TO THE STUDENT.
THE CORE SWITCH AND SWITCH/ROUTER FARM SWITCHES TRUNK TRAFFIC BETWEEN THE STUDENT L3 SWITCH AND ROUTER, MAKING IT APPEAR AS THOUGH THET ARE DIRECTLY CONNECTED. THE 2xx VLAN PASSING BETWEEN THEM ALLOWS FOR THE OSPF NEIGHBOR TO BE ESTABLISHED AND ALLOWS THE STUDENT ACCESS TO THEIR ROUTER.
TRAFFIC IS TRUNKED ACROSS THE FARM SWITCHES AND THROUGH THE CORE SWITCH TO THE INSTRUCTOR AGGREGATE SWITCH WHICH ALLOWS LAYER 2 CONNECTIVITY TO ALL OF THE UPLINK NODES AND CORE NODES THE STUDENTS FORM TUNNELS AND ADJACENCIES WITH. THE LAYER 3 CONNECTIVITY ESTABLISHED CREATES A PATH TO THE DATA CENTER RESOURCES AND OTHER LAB NODES.
IN LABs 8-11 EACH STUDENT OBTAINS ACCESS TO AN MPLS NODE (ANOTHER LAYER 3 SWITCH) WHICH IS UTILIZED IN THOSE HIGHER LEVEL LABS.

## Slide 19: TEMPLATE FOR IPV6 DMVPN (SPOKE) WITH OSPFv3
interface Tunnel XXXXX
description XXXXX
ipv6 address FE80::X link-local
ipv6 address X:X:X:X:X:X:X:X /X
ipv6 enable
ipv6 mtu XXXX
ipv6 nhrp authentication XXXXXXX
ipv6 nhrp network-id XXXXXXX
ipv6 nhrp shortcut
ipv6 nhrp nhs X:X:X:X:X:X:X:X nbma X:X:X:X:X:X:X:X
ipv6 nhrp map multicast X:X:X:X:X:X:X:X
qos pre-classify
ospfv3 network point-to-multipoint
ospfv3 hello-interval XXX
ospfv3 dead-interval XXX
ospfv3 priority XXX
ospfv3 cost XXX
ospfv3 flood-reduction
ospfv3 XXX ipv6 area XXX
tunnel source XXXXXXX
tunnel mode gre multipoint ipv6
tunnel key XXXXX
tunnel path-mtu-discovery
TEMPLATE FOR SNMPv2 AGENT CONFIG
Snmp-server community XXXXXX ro [access-list name/number]
Snmp-server community XXXXXX rw [access-list name/number]
TEMPLATE FOR SNMPv3 AGENT CONFIG
Snmp-server view XXXXX iso included
Snmp-server group XXXXX v3 priv
Snmp-server user XXXXX [group] v3 auth sha XXXXX priv aes 128 XXXXX access [access-list name/number]
EXAMPLE (SNMPV3)
Snmp-server view NETWORK iso included
Snmp-server group STUDENTS v3 priv
snmp-server user NETOPS STUDENTS v3 auth sha P@$$WorD priv aes 128 PA$$wO#d access 101
EXAMPLE (SNMPV2)
Snmp-server community FORTGORDON ro 101
Snmp-server community NODROGTROF rw 102